## Slide 1: EEL 3135 Systems and Signals
Applications to Feedback and Controls
Notes: Frame this section as an application of transfer functions and pole analysis. The goal is to understand what closing a loop changes, not to teach a complete control-design course.

## Slide 2
Why close the loop?
2
Open loop
The system acts without comparing its output with the desired value. Plant changes or disturbances directly change the result.
Feedback loop
The measured output returns to the summing junction. The error signal drives the plant toward the reference.
Feedback can improve tracking and reduce some disturbances. It also moves the poles and changes the transient response.
Feedback changes the system dynamics. It does not merely correct the output value.
Notes: Ask students for examples such as cruise control or temperature control. Then move immediately to the question that connects with prior material: what happens to the poles when the loop closes?

## Slide 3
Negative-feedback interconnection
3
R(s)
+
G(s)
Y(s)
H(s)
E(s)
−
E(s) = R(s) − H(s)Y(s)
Y(s) = G(s)E(s)
The feedback-path model is H(s). A gain inside G(s) remains a forward-path gain.
Notes: Emphasize the signal roles. G(s) is the forward path. H(s) is the feedback path. This addresses the common confusion between a controller gain in G(s) and a feedback-path gain.

## Slide 4
Closed-loop transfer function
4
Y(s) = G(s)[R(s) − H(s)Y(s)]
[1 + G(s)H(s)]Y(s) = G(s)R(s)
T(s) = Y(s)/R(s) = G(s)/[1 + G(s)H(s)]
Unity feedback: H(s) = 1
The denominator changes when the loop closes.
Notes: Derive the expression line by line rather than presenting it as a memorized formula. The denominator is the bridge to the next slide on closed-loop poles.

## Slide 5
Closed-loop poles and stability
5
Characteristic equation
1 + G(s)H(s) = 0
Its roots are the closed-loop poles. They determine decay, oscillation, and stability after feedback is connected.
The poles of G(s) alone are not the closed-loop poles.
For a causal rational closed loop:
All poles in the open left half-plane
Stable
Any pole in the right half-plane
Unstable
Simplify the closed-loop transfer function before classifying its poles.
Notes: Return to the pole-pattern language students already know. The only new step is forming the closed-loop denominator.

## Slide 6
Gain example: G(s) = K/[s(s + 2)]
6
Unity feedback gives
T(s) = K/(s² + 2s + K)
Poles: s = −1 ± √(1 − K)
K = 0.5: two negative real poles
K = 1: repeated pole at −1
K = 4: poles at −1 ± j√3
Compare s² + 2s + K with
s² + 2ζωₙs + ωₙ²
ωₙ = √K
ζ = 1/√K
Larger K increases natural frequency and reduces damping ratio.
Changing gain moves the closed-loop poles and changes the response shape.
Notes: Have students classify each pole pattern before discussing step responses. This makes the later plot a confirmation of their prediction.

## Slide 7
Activity 1: Classify the closed-loop response
7
A unity-feedback system has G(s) = 4/[s(s + 2)]. Which description is correct?
A. Unstable because the forward path contains an integrator
B. Stable and overdamped with two real poles
C. Stable and underdamped with poles at −1 ± j√3
D. Undamped because the closed-loop poles are imaginary
Form the closed-loop denominator before classifying the poles.
Notes: Correct answer: C. T(s)=4/(s^2+2s+4), whose poles are -1 plus or minus j square root of 3.

## Slide 8
Gain changes the step response
8
K = 0.5
Slow overdamped response
K = 1
Fastest response without oscillation
K = 4
Faster initial rise with overshoot
Chart: Unit-step response
| 0.00 | 0.15 | 0.30 | 0.45 | 0.60 | 0.75 | 0.90 | 1.05 | 1.20 | 1.35 | 1.50 | 1.65 | 1.80 | 1.95 | 2.10 | 2.25 | 2.40 | 2.55 | 2.70 | 2.85 | 3.00 | 3.15 | 3.30 | 3.45 | 3.60 | 3.75 | 3.90 | 4.05 | 4.20 | 4.35 | 4.50 | 4.65 | 4.80 | 4.95 | 5.10 | 5.25 | 5.40 | 5.55 | 5.70 | 5.85 | 6.00
K = 0.5 | -3.6082e-16 | 0.0050976 | 0.018535 | 0.038019 | 0.061795 | 0.088519 | 0.11717 | 0.14696 | 0.17732 | 0.2078 | 0.23807 | 0.26789 | 0.29709 | 0.32555 | 0.35318 | 0.37993 | 0.40577 | 0.43068 | 0.45467 | 0.47773 | 0.49989 | 0.52116 | 0.54156 | 0.56113 | 0.57989 | 0.59787 | 0.61509 | 0.63159 | 0.64738 | 0.66251 | 0.677 | 0.69086 | 0.70414 | 0.71684 | 0.72901 | 0.74065 | 0.75179 | 0.76245 | 0.77266 | 0.78243 | 0.79178
K = 1 | 0 | 0.010186 | 0.036936 | 0.075439 | 0.1219 | 0.17336 | 0.22752 | 0.28263 | 0.33737 | 0.39079 | 0.44217 | 0.49107 | 0.53716 | 0.58029 | 0.62039 | 0.65745 | 0.69156 | 0.72281 | 0.75134 | 0.7773 | 0.80085 | 0.82216 | 0.8414 | 0.85873 | 0.87431 | 0.88829 | 0.90081 | 0.91202 | 0.92202 | 0.93095 | 0.9389 | 0.94598 | 0.95227 | 0.95785 | 0.96281 | 0.9672 | 0.97109 | 0.97454 | 0.97758 | 0.98027 | 0.98265
K = 4 | 0 | 0.040519 | 0.14458 | 0.28769 | 0.44868 | 0.61049 | 0.76043 | 0.88999 | 0.99446 | 1.0723 | 1.1244 | 1.1533 | 1.163 | 1.1575 | 1.1413 | 1.1184 | 1.0923 | 1.0659 | 1.0412 | 1.0197 | 1.0023 | 0.9892 | 0.98034 | 0.97529 | 0.97346 | 0.97415 | 0.97666 | 0.98032 | 0.98455 | 0.98887 | 0.99293 | 0.99649 | 0.99939 | 1.0016 | 1.0031 | 1.004 | 1.0043 | 1.0042 | 1.0039 | 1.0033 | 1.0026
The pole prediction explains the waveform before the simulation is shown.
Notes: Reveal the curves after students predict them from slide 6. Point out that larger gain is not equivalent to uniformly better performance.

## Slide 9
Reference tracking and final value
9
Unit-step reference: R(s) = 1/s
y(∞) = lim sT(s)R(s) = T(0)
s→0
For T(s) = K/(s² + 2s + K),
T(0) = 1 for K > 0.
The stable closed loop reaches a unit-step reference with zero steady-state error.
Check the poles of sY(s) before applying the final-value theorem.
Tracking performance and stability must be checked together.
Notes: Use the final-value theorem as a response check. Do not let the DC gain calculation replace the closed-loop stability check.

## Slide 10
Output disturbance rejection
10
Y(s) = G(s)[R(s) − Y(s)] + D(s)
Y(s) = G(s)/[1 + G(s)] R(s) + 1/[1 + G(s)] D(s)
Sensitivity function
S(s) = 1/[1 + G(s)]
Large |G(jω)| makes |S(jω)| small at that frequency, so the loop reduces an output disturbance there.
Disturbance rejection depends on frequency.
Notes: Specify that D(s) enters at the plant output. The disturbance transfer changes if the disturbance enters at another location.

## Slide 11
Measurement noise and complementary sensitivity
11
Measurement noise N(s) enters the feedback measurement.
Y(s) = G(s)/[1 + G(s)] R(s) − G(s)/[1 + G(s)] N(s)
T(s) = G(s)/[1 + G(s)]
S(s) = 1/[1 + G(s)]
S(s) + T(s) = 1
Strong tracking at a frequency can also transmit measurement noise at that frequency.
Notes: Keep this qualitative. The identity S+T=1 shows why feedback design involves tradeoffs rather than making every unwanted effect small at once.

## Slide 12
Gain tradeoffs
12
Lower loop gain
Less disturbance rejection
Larger tracking error
Often more damping
Higher loop gain
Better low-frequency tracking
Better low-frequency disturbance rejection
Possible overshoot or instability
The closed-loop poles decide the transient cost of increasing gain.
Larger gain is a design choice, not a guarantee of better behavior.
Notes: Connect each tradeoff to the equations already shown. Avoid presenting gain as good or bad by itself.

## Slide 13
Activity 2: Identify the disturbance path
13
A disturbance D(s) is added at the plant output of a unity-feedback system. Which transfer function maps D(s) to Y(s)?
A. G(s)
B. G(s)/[1 + G(s)]
C. 1/[1 + G(s)]
D. 1/G(s)
Write the output equation before selecting the path.
Notes: Correct answer: C. An output disturbance passes through the sensitivity function 1/(1+G) for unity feedback.

## Slide 14
Scope for Systems and Signals
14
Core course skills
Derive G/(1 + GH)
Find the closed-loop poles
Predict stability and transient form
Interpret tracking and disturbance paths
Explain gain tradeoffs
Dedicated controls course
Root locus
Nyquist stability
Gain and phase margins
Controller synthesis
Robust control design
This section applies pole analysis. It does not need a full control-design unit.
Notes: Use this slide to set expectations. Students should understand the system consequences of feedback without being asked to design a controller from specifications.

## Slide 15
Feedback skills to retain
15
Form the closed-loop transfer function from the block diagram
Use 1 + G(s)H(s) = 0 to find the closed-loop poles
Predict stability and damping from those poles
Use final values only after checking stability
Identify reference, disturbance, and noise transfer paths
Treat gain changes as tradeoffs
Closing the loop changes the poles. The poles explain the resulting behavior.
Notes: Close with retrieval. Ask students to explain why the poles of G(s) alone cannot predict the closed-loop response.