## Slide 1: EEL 3135 Systems and Signals
Frequency Response of an LTIC System
Notes: Frame frequency response as a shortcut for predicting the long-term response to a sinusoid. The shortcut should follow from the total causal response rather than appear as an unexplained rule.

## Slide 2
A sinusoidal-input question
2
Input
x(t) = A cos(ω₀t + φ)
What output frequency remains after transients decay?
How does the system change amplitude?
How does the system change phase?
Frequency response answers all three questions by evaluating the transfer function at s = jω₀.
For a stable system, the system-pole terms decay and the sinusoidal input terms remain.
The steady-state output keeps the input frequency.
Notes: Ask students to predict the output frequency before writing H(jω). This reinforces the complex-exponential eigenfunction idea.

## Slide 3
Complex exponentials are LTI eigenfunctions
3
Input: x(t) = eʲωᵗ
y(t) = ∫ h(τ)eʲω⁽ᵗ⁻τ⁾ dτ
= eʲωᵗ ∫ h(τ)e⁻ʲωτ dτ
= H(jω)eʲωᵗ
The waveform keeps the same exponential form. The complex number H(jω) supplies the amplitude scale and phase shift.
An LTIC system multiplies each complex sinusoid by H(jω).
Notes: This derivation avoids residues. Students already know convolution, so factor the common exponential and identify the remaining integral as H(jω).

## Slide 4
Real sinusoidal steady state
4
x(t) = A cos(ω₀t + φ)
H(jω₀) = |H(jω₀)|eʲᶿ
yₛₛ(t) = A|H(jω₀)| cos(ω₀t + φ + θ)
Output amplitude
A|H(jω₀)|
Output phase
φ + ∠H(jω₀)
Magnitude changes amplitude. Phase changes timing. Frequency remains ω₀.
Notes: State the formula only after the complex-exponential derivation. Keep the input phase phi so students see that the system phase adds to it.

## Slide 5
Causal sinusoidal input
5
x(t) = A cos(ω₀t)u(t)
X(s) has poles at s = ±jω₀
Y(s) = H(s)X(s)
System-pole terms
Transient response
Decay if the system is stable
Input-pole terms at ±jω₀
Sinusoidal steady state
Remain after transients decay
The complete causal response contains transient and steady-state terms.
Notes: This slide provides the missing bridge between Y=HX and the steady-state shortcut. Students should identify which poles produce each part before doing partial fractions.

## Slide 6
Worked example: complete causal response
6
H(s) = 4/(s + 4)
x(t) = 3 cos(2t)u(t)
X(s) = 3s/(s² + 4)
Y(s) = 12s/[(s + 4)(s² + 4)]
Y(s) = −2.4/(s + 4) + (2.4s + 2.4)/(s² + 4)
y(t) = [−2.4e⁻⁴ᵗ + 2.4 cos(2t) + 1.2 sin(2t)]u(t)
y(0⁺) = 0
The −4 pole produces the transient. The ±j2 poles produce the sinusoidal steady state.
Notes: Before revealing the partial fractions, ask students to predict one decaying exponential plus cosine and sine terms at 2 rad/s.

## Slide 7
Transient and steady-state components
7
y_tr(t) = −2.4e⁻⁴ᵗ
y_ss(t) = 2.4 cos(2t) + 1.2 sin(2t)
y_ss(t) = (6/√5) cos[2t − tan⁻¹(1/2)]
After the transient decays, only the sinusoid remains.
Chart: Complete response
Steady state describes what remains, not the complete response immediately after t = 0.
Notes: Use the graph to show why the total curve initially differs from the steady-state sinusoid. The difference is the decaying system-pole term.

## Slide 8
Activity 1: Identify the response components
8
For the response below, which term is the transient?
y(t) = [−2.4e⁻⁴ᵗ + 2.4 cos(2t) + 1.2 sin(2t)]u(t)
A. −2.4e⁻⁴ᵗ
B. 2.4 cos(2t)
C. 1.2 sin(2t)
D. Both sinusoidal terms
Find the term generated by the stable system pole.
Notes: Correct answer: A. The pole at -4 produces the decaying exponential. The input poles at plus and minus j2 produce the cosine and sine terms.

## Slide 9
Direct evaluation with H(jω)
9
H(j2) = 4/(4 + j2)
|H(j2)| = 4/√20 = 2/√5
∠H(j2) = −tan⁻¹(1/2)
Input amplitude: 3
Output amplitude: 3(2/√5) = 6/√5
Output phase: −tan⁻¹(1/2)
y_ss(t) = (6/√5) cos[2t − tan⁻¹(1/2)]
H(jω) gives the steady-state sinusoid without calculating the transient.
Notes: Compare this result with slide 7. The shortcut and the partial-fraction calculation produce the same steady-state sinusoid.

## Slide 10
Phase shift in the time domain
10
H(j2) has phase −26.6°. The output lags the input.
Equivalent time shift: Δt = 26.6°/(360° · f)
Chart: Input and steady-state output
Phase angle describes a timing shift relative to the input sinusoid.
Notes: Students do not need to convert every phase to seconds. The graph helps them interpret a negative phase as lag for this positive frequency.

## Slide 11
Frequency sweep of a first-order system
11
H(s) = 4/(s + 4)
Chart: Magnitude
| 0.1 | 0.15 | 0.23 | 0.35 | 0.54 | 0.83 | 1.3 | 1.9 | 2.9 | 4.5 | 6.8 | 10 | 16 | 24 | 37 | 56 | 86 | 131 | 200
magnitude | 0.99969 | 0.99927 | 0.99831 | 0.99609 | 0.99097 | 0.97937 | 0.95387 | 0.90151 | 0.80686 | 0.66711 | 0.50631 | 0.35924 | 0.24471 | 0.16325 | 0.10786 | 0.070952 | 0.046586 | 0.030563 | 0.020043
Chart: Phase
| 0.1 | 0.15 | 0.23 | 0.35 | 0.54 | 0.83 | 1.3 | 1.9 | 2.9 | 4.5 | 6.8 | 10 | 16 | 24 | 37 | 56 | 86 | 131 | 200
phase | -1.4321 | -2.1837 | -3.3284 | -5.0691 | -7.7049 | -11.6594 | -17.4704 | -25.6427 | -36.2101 | -48.1559 | -59.582 | -68.9463 | -75.8353 | -80.6042 | -83.8081 | -85.9313 | -87.3299 | -88.2486 | -88.8515
Low frequencies pass with little change. High frequencies are attenuated and delayed more strongly.
Notes: This slide introduces the idea of frequency-selective behavior without yet teaching Bode construction. The next deck explains logarithmic axes, decibels, and asymptotes.

## Slide 12
Activity 2: Predict a steady-state output
12
H(j3) = 0.4e⁻ʲπ⁄⁶
x(t) = 5 cos(3t + π/4)
A. 2 cos(3t + π/12)
B. 2 cos(3t + 5π/12)
C. 5 cos(3t − π/6)
D. 0.4 cos(3t + π/4)
Multiply amplitudes and add phases.
Notes: Correct answer: A. The amplitude is 5 times 0.4, which equals 2. The phase is pi over 4 minus pi over 6, which equals pi over 12.

## Slide 13
Conditions and interpretation
13
Stable system
System-pole terms decay. The sinusoidal term describes the long-term output.
Finite H(jω₀)
A pole at jω₀ invalidates the bounded steady-state formula. A zero at jω₀ can eliminate the steady-state output.
Nonzero initial conditions add a zero-input response. For a stable system, that contribution also decays.
H(jω) predicts sinusoidal steady state, not every term in the initial transient.
Notes: Use this slide to prevent overgeneralization. The formula is powerful because it answers a specific long-term question.

## Slide 14
Frequency-response skills to retain
14
Use complex exponentials to explain why frequency is preserved
Separate system-pole transients from input-pole sinusoidal terms
Evaluate H(jω) at the input frequency
Scale the input amplitude by |H(jω)|
Add ∠H(jω) to the input phase
Check stability and initial-condition assumptions
The next step is the Bode plot, which displays H(jω) across many frequencies.
Notes: Close by linking this deck to the Bode-plot deck. Frequency response supplies the meaning. Bode plots supply an efficient visual representation and construction method.