## Slide 1: EEL 3135 Systems and Signals
Frequency Response and Bode Plots
Notes: Introduce the goal in plain language. Students will learn to predict what the system does to sinusoids and to sketch the important Bode features without plotting many individual points.

## Slide 2
A filter question before the mathematics
2
A sensor contains useful slow variations and unwanted high-frequency noise.
Which frequencies should pass?
Which frequencies should be reduced?
How much phase shift should we expect?
A Bode plot answers these questions for many sinusoidal inputs on one pair of graphs.
Chart: Example low-pass magnitude
| 0.01 | 0.02 | 0.03 | 0.06 | 0.1 | 0.18 | 0.32 | 0.56 | 1 | 1.8 | 3.2 | 5.6 | 10 | 18 | 32 | 56 | 100
magnitude | -0.00043427 | -0.0013731 | -0.0043408 | -0.013712 | -0.043214 | -0.13521 | -0.41393 | -1.1933 | -3.0103 | -6.1933 | -10.4139 | -15.1352 | -20.0432 | -25.0137 | -30.0043 | -35.0014 | -40.0004
The plot gives a physical answer before it becomes a construction exercise.
Notes: Begin with the sensor question. Ask students to point to a low, middle, and high frequency on the plot and describe what happens to each input. Do not introduce slope rules yet.

## Slide 3
Sinusoidal steady-state response
3
Input
x(t) = A cos(ω₀t + φ)
Evaluate the system
H(jω₀) = |H(jω₀)|eʲᶿ
Steady-state output
yₛₛ(t) = A|H(jω₀)|
cos(ω₀t + φ + θ)
Magnitude changes amplitude
Phase shifts the sinusoid
The system must be stable for its transient terms to decay.
The output keeps the input frequency. Only amplitude and phase change.
Notes: Connect this formula to the frequency-response material. The Bode plot is a convenient way to read the two quantities |H(jω)| and angle H(jω) across many frequencies.

## Slide 4
Anatomy of a Bode plot
4
Chart: Magnitude
| 0.01 | 0.02 | 0.03 | 0.06 | 0.1 | 0.18 | 0.32 | 0.56 | 1 | 1.8 | 3.2 | 5.6 | 10 | 18 | 32 | 56 | 100
magnitude | -0.00043427 | -0.0013731 | -0.0043408 | -0.013712 | -0.043214 | -0.13521 | -0.41393 | -1.1933 | -3.0103 | -6.1933 | -10.4139 | -15.1352 | -20.0432 | -25.0137 | -30.0043 | -35.0014 | -40.0004
Chart: Phase
| 0.01 | 0.02 | 0.03 | 0.06 | 0.1 | 0.18 | 0.32 | 0.56 | 1 | 1.8 | 3.2 | 5.6 | 10 | 18 | 32 | 56 | 100
phase | -0.57294 | -1.0188 | -1.8112 | -3.2186 | -5.7106 | -10.0834 | -17.5484 | -29.3508 | -45 | -60.6492 | -72.4516 | -79.9166 | -84.2894 | -86.7814 | -88.1888 | -88.9812 | -89.4271
Equal horizontal distances represent equal frequency ratios, such as 1 to 10 and 10 to 100.
Notes: Explain the logarithmic axis as a ratio axis. One decade means multiplying frequency by ten. Magnitude reports amplitude ratio in dB. Phase reports the angle added to the input sinusoid.

## Slide 5
Activity 1: Predict the output sinusoid
5
At ω = 10 rad/s, a Bode plot gives
|H(j10)| = −6 dB and ∠H(j10) = −45°
Input: x(t) = 4 cos(10t + 20°)
A. 4 cos(10t − 25°)
B. 2 cos(10t − 25°)
C. 2 cos(10t − 65°)
D. −6 cos(10t − 45°)
Convert −6 dB to an amplitude ratio, then add the phases.
Notes: Correct answer: B. A magnitude of -6 dB is approximately 0.5, so the output amplitude is 2. The output phase is 20 degrees plus -45 degrees, which equals -25 degrees.

## Slide 6
Decibels as amplitude ratios
6
M_dB(ω) = 20 log₁₀|H(jω)|
Amplitude ratio | Magnitude | Meaning
10 | +20 dB | ten times the amplitude
2 | approximately +6 dB | twice the amplitude
1 | 0 dB | no amplitude change
1/√2 | approximately −3 dB | corner of a first-order pole
1/2 | approximately −6 dB | half the amplitude
0.1 | −20 dB | one tenth of the amplitude
A negative decibel value means attenuation. It does not mean a negative amplitude.
Notes: Keep the conversion table visible while students answer Activity 1. Emphasize 0 dB as a ratio of one and -3 dB as the exact first-order corner value.

## Slide 7
First-order pole
7
H(s) = 1/(1 + s/ωₚ)
ω ≪ ωₚ: 0 dB
ω = ωₚ: −3 dB and −45°
ω ≫ ωₚ: slope −20 dB/decade
Above the corner, |H| ≈ ωₚ/ω. A tenfold frequency increase gives a tenfold amplitude decrease.
Chart: Exact curve and straight-line approximation
| 0.01 | 0.02 | 0.03 | 0.06 | 0.1 | 0.18 | 0.32 | 0.56 | 1 | 1.8 | 3.2 | 5.6 | 10 | 18 | 32 | 56 | 100
exact | -0.00043427 | -0.0013731 | -0.0043408 | -0.013712 | -0.043214 | -0.13521 | -0.41393 | -1.1933 | -3.0103 | -6.1933 | -10.4139 | -15.1352 | -20.0432 | -25.0137 | -30.0043 | -35.0014 | -40.0004
asymptote | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | -5 | -10 | -15 | -20 | -25 | -30 | -35 | -40
A real pole bends the magnitude downward after its corner frequency.
Notes: Derive the slope from the high-frequency approximation. The -20 dB per decade rule should follow from the formula rather than appear as a fact to memorize.

## Slide 8
First-order zero
8
H(s) = 1 + s/ω_z
ω ≪ ω_z: 0 dB
ω = ω_z: +3 dB and +45°
ω ≫ ω_z: slope +20 dB/decade
A pole adds negative slope and phase. A zero adds positive slope and phase.
Chart: Exact curve and straight-line approximation
| 0.01 | 0.02 | 0.03 | 0.06 | 0.1 | 0.18 | 0.32 | 0.56 | 1 | 1.8 | 3.2 | 5.6 | 10 | 18 | 32 | 56 | 100
exact | 0.00043427 | 0.0013731 | 0.0043408 | 0.013712 | 0.043214 | 0.13521 | 0.41393 | 1.1933 | 3.0103 | 6.1933 | 10.4139 | 15.1352 | 20.0432 | 25.0137 | 30.0043 | 35.0014 | 40.0004
asymptote | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 5 | 10 | 15 | 20 | 25 | 30 | 35 | 40
A real zero bends the magnitude upward after its corner frequency.
Notes: Ask students to compare this slide with the previous pole slide. The rules are mirror images, but their signs matter.

## Slide 9
Core Bode building blocks
9
Factor | Magnitude contribution | Phase contribution
positive gain K | vertical shift of 20 log₁₀K dB | 0°
s | +20 dB/decade from the start | +90°
1/s | −20 dB/decade from the start | −90°
1 + s/ω_z | +20 dB/decade after ω_z | 0° toward +90°
1/(1 + s/ωₚ) | −20 dB/decade after ωₚ | 0° toward −90°
Factor magnitudes add in decibels. Their phase angles also add.
Notes: Do not ask students to memorize every row immediately. Use the table while building the worked example, then return to it as a summary.

## Slide 10
Activity 2: Predict the high-frequency slope
10
H(s) = 10/[(1 + s/2)(1 + s/20)]
What is the magnitude slope well above 20 rad/s?
A. 0 dB/decade
B. −20 dB/decade
C. −40 dB/decade
D. +20 dB/decade
Count the pole and zero factors that are active at that frequency.
Notes: Correct answer: C. Above 20 rad/s, both real poles contribute -20 dB per decade, giving a net slope of -40 dB per decade.

## Slide 11
Worked example: gain, corners, and slopes
11
H(s) = 10(1 + s/10)/[(1 + s)(1 + s/100)]
Low-frequency gain: 10 = 20 dB
Corner frequencies: 1, 10, and 100 rad/s
Frequency range | Active factors | Net slope
ω < 1 | none | 0 dB/decade
1 < ω < 10 | pole at 1 | −20 dB/decade
10 < ω < 100 | pole at 1 and zero at 10 | 0 dB/decade
ω > 100 | two poles and one zero | −20 dB/decade
Mark the corners first. Then update the slope one factor at a time.
Notes: Pause before revealing the table. Ask students to predict each slope region using the building-block table from slide 9.

## Slide 12
Worked example: magnitude plot
12
20 dB below 1 rad/s
Falls to about 0 dB by 10 rad/s
Nearly flat from 10 to 100 rad/s
Falls again above 100 rad/s
The exact curve rounds each corner. The straight-line sketch captures the main structure.
Chart: Exact response and asymptotic sketch
| 0.01 | 0.02 | 0.03 | 0.06 | 0.1 | 0.18 | 0.32 | 0.56 | 1 | 1.8 | 3.2 | 5.6 | 10 | 18 | 32 | 56 | 100 | 178 | 316 | 562 | 1000 | 1778 | 3162 | 5623 | 10000
exact | 19.9996 | 19.9986 | 19.9957 | 19.9864 | 19.9572 | 19.8662 | 19.5904 | 18.8203 | 17.0325 | 13.9405 | 9.9957 | 6.0444 | 2.9239 | 1.0444 | -0.0043408 | -1.0595 | -2.9675 | -6.1797 | -10.4096 | -15.1338 | -20.0428 | -25.0136 | -30.0043 | -35.0014 | -40.0004
asymptote | 20 | 20 | 20 | 20 | 20 | 20 | 20 | 20 | 20 | 15 | 10 | 5 | 0 | 0 | 0 | 0 | 0 | -5 | -10 | -15 | -20 | -25 | -30 | -35 | -40
The hand sketch predicts the regions. Software verifies the smooth transitions.
Notes: Have students compare the exact and approximate curves. The asymptote is a reasoning tool, not an exact replacement for the frequency response.

## Slide 13
Worked example: phase and output
13
∠H(jω) = tan⁻¹(ω/10) − tan⁻¹(ω) − tan⁻¹(ω/100)
At ω = 10 rad/s
|H(j10)| ≈ 1.40
∠H(j10) = −45°
x(t) = 2 cos(10t)
yₛₛ(t) ≈ 2.80 cos(10t − 45°)
Chart: Exact phase response
| 0.01 | 0.02 | 0.03 | 0.06 | 0.1 | 0.18 | 0.32 | 0.56 | 1 | 1.8 | 3.2 | 5.6 | 10 | 18 | 32 | 56 | 100 | 178 | 316 | 562 | 1000 | 1778 | 3162 | 5623 | 10000
phase | -0.52137 | -0.92707 | -1.6482 | -2.9286 | -5.195 | -9.1665 | -15.9183 | -26.4545 | -39.8623 | -51.5845 | -56.7144 | -53.7844 | -45 | -36.2156 | -33.2856 | -38.4155 | -50.1377 | -63.5455 | -74.0817 | -80.8335 | -84.805 | -87.0714 | -88.3518 | -89.0729 | -89.4786
Read magnitude and phase at the input frequency, then apply both to the sinusoid.
Notes: This slide closes the loop from a transfer function to a time-domain prediction. Students should identify the unchanged frequency, the amplitude scale, and the phase shift.

## Slide 14
Activity 3: Interpret a measured Bode point
14
At 5 rad/s, the Bode plot shows +6 dB and −30°.
Input: x(t) = 3 cos(5t + 10°)
A. 6 cos(5t − 20°)
B. 3 cos(5t − 30°)
C. 6 cos(5t − 40°)
D. 9 cos(5t + 40°)
+6 dB is approximately a factor of two. Add the input phase and system phase.
Notes: Correct answer: A. The magnitude doubles the input amplitude from 3 to 6. The phase becomes 10 degrees plus -30 degrees, which equals -20 degrees.

## Slide 15
Complex poles connect ringing and resonance
15
H(s) = ωₙ²/(s² + 2ζωₙs + ωₙ²)
Poles: −ζωₙ ± jωₙ√(1 − ζ²)
Smaller ζ moves the poles closer to the imaginary axis. The natural response rings longer. The frequency response develops a larger peak.
Example: ωₙ = 10 rad/s
Chart: Second-order magnitude response
| 0.1 | 0.13 | 0.17 | 0.23 | 0.3 | 0.39 | 0.51 | 0.67 | 0.88 | 1.2 | 1.5 | 2 | 2.6 | 3.4 | 4.5 | 5.9 | 7.7 | 10 | 13 | 17 | 23 | 30 | 39 | 51 | 67 | 88 | 116 | 152 | 200
ζ = 0.2 | 0.00079913 | 0.0013751 | 0.0023664 | 0.0040722 | 0.0070081 | 0.012062 | 0.020764 | 0.035755 | 0.061599 | 0.10622 | 0.18343 | 0.31761 | 0.55246 | 0.96861 | 1.7219 | 3.1323 | 5.8173 | 7.88 | 0.75054 | -6.5532 | -12.6237 | -18.0641 | -23.1802 | -28.1214 | -32.9654 | -37.7544 | -42.5118 | -47.2511 | -51.9799
ζ = 0.5 | 0.00043427 | 0.00074724 | 0.0012857 | 0.0022122 | 0.0038058 | 0.0065468 | 0.011259 | 0.019356 | 0.033251 | 0.057053 | 0.09768 | 0.16657 | 0.28189 | 0.4697 | 0.75574 | 1.1095 | 1.2019 | -0.072603 | -3.6374 | -8.4821 | -13.5502 | -18.5443 | -23.4412 | -28.2673 | -33.0483 | -37.8019 | -42.5392 | -47.267 | -51.9891
ζ = 1.0 | -0.00086855 | -0.0014945 | -0.0025715 | -0.0044243 | -0.0076117 | -0.013094 | -0.022518 | -0.038712 | -0.066507 | -0.11413 | -0.19546 | -0.33366 | -0.56643 | -0.95293 | -1.5802 | -2.5637 | -4.0322 | -6.0923 | -8.7844 | -12.063 | -15.819 | -19.9237 | -24.263 | -28.7516 | -33.3321 | -37.9676 | -42.6358 | -47.3232 | -52.0218
The same pole locations explain transient ringing and frequency-domain peaking.
Notes: Connect this slide directly to the earlier pole-pattern lesson. Do not derive the resonance formula here. Ask students to compare the three damping ratios and explain the change in the peak.

## Slide 16
Bode-plot skills to retain
16
Read magnitude and phase at the input frequency
Convert decibels to an amplitude ratio
Find corner frequencies from normalized poles and zeros
Update the magnitude slope after each corner
Use a hand sketch to predict the main structure
Use software to verify exact curves and resonance
Inspect the poles and zeros first. Detailed plotting comes after the prediction.
Notes: Use this as the closing retrieval slide. Ask students to explain one item in their own words and identify which skill still needs practice.